## Slide 1: Project 3 Phase 1: Implementation A* algorithm for a mobile Robot
This is a group project (max two students)
Due Date – March 21st, 11.59 PM

## Slide 2
Project3

## Slide 3: Action Set
30◦
Consecutive angles are 30 degrees.
30◦
To check for duplicate nodes:
Euclidean distance threshold is 0.5 unit (for x, y)
Theta threshold is 30 degrees (for Ѳ)
Python file provided can be used to plot
L

## Slide 4
Front
Front

## Slide 5: Project 3 Description
1) Check the feasibility of all inputs/outputs (if user gives start and goal nodes that are in the obstacle space they should be informed by a message and they should try again). (retain from previous project)
2) Implement A* Algorithm to find a path between start and end point on a given map for a mobile robot (radius = 10; clearance = 5).
3) Your code must output an animation of optimal path generation between start and goal point on the map. You need to show both the node exploration as well as the optimal path generated. (Some useful tools for simulation are OpenCV/Pygame/Matplotlib). (sample code using Matplotlib is provided)

## Slide 6: Step 0: Get the Inputs from the User
Your code must take following values from the user:
Start Point Co-ordinates (3-element vector): (Xs,Ys,Theta_s)
Goal Point Co-ordinates (3-element vector): (Xg,Yg, Theta_g**)
Clearance and robot radius
Step size of movement in units ( 1 <= L <=10)
* Cartesian Coordinates should be used
**Theta_g & Theta in degrees.

## Slide 7: Theta_g and Theta
Theta_g is the orientation at goal point of the robot.
Theta is the angle between the action set at each node.
Take these parameters as user inputs (k*30), i.e. {…,-60,-30,0,30,60,…}

## Slide 8: Step 1) Define the actions in a mathematical format
Use can use the same data structure from project 1 to store the node information.
Write 5 subfunctions, one for each action. The output of each subfunction is the state of a new node after taking the associated action.
Step size is the length of the vectors.
30
30
L

## Slide 9: Step 2) Find mathematical representation of free space (Retain from previous project)
Use Half planes and semi-algebraic models to represent the obstacle space.

## Slide 10: Step 3): implement A* search algorithm to search the tree and to find the optimal path
Forward search
Consider Euclidean distance as a heuristic function.
Note - You have to define a reasonable threshold value for the distance to the goal point. Due to the limited number of moves, the robot cannot reach the exact goal location, so to terminate the program a threshold distance has to be defined.
Goal threshold (1.5 units radius)

## Slide 11: Step 3 (Continue) - Graph
Start
Goal
Threshold distance

## Slide 12: Generate the graph
Consider the configuration space as a 3 dimensional space.
First method for finding the duplicate node: In order to limit the number of the nodes, before adding the node make sure that the distance of the new node is greater than the threshold in x, y, and theta dimensions with respect to all existing nodes. This method is very slow. You should avoid using this method.
Second method for finding the duplicate node: Use a matrix to store the information of the visited nodes. For threshold of 0.5 unit for x and y, and threshold of 30 degree for Theta in the given map, you should use a matrix V with 250/(threshold) by 400/(threshold) by 12 (i.e. 360/30) to store the visited regions information i.e. your matrix dimension will be (500x800x12).
Example:
Set V[i][j][k]=0.
If node1= (3.2, 4.7, 0) visited  visited region: (3, 4.5, 0) V[6][9][0]=1
If node2= (10.2, 8.8, 30) visited  visited region: (10, 9, 30)  V[20][18][1]=1
If node3= (10.1, 8.9, 30) visited  visited region: (10, 9, 30)  V[20][18][1]=1
(Here node2 and node 3 are duplicate nodes)

## Slide 13: Step 4) Find the optimal path (Backtracking) (Retain from previous project)
Write a subfunction that compares the current node with the goal node and return TRUE if they are equal.
While generating each new node this subfunction should be called
Write a subfunction that once the goal node is reached, using the child and parent relationship, it backtracks from the goal node to initial node and outputs all the intermediate nodes.

## Slide 14: Step 5) Represent the optimal path (Retain from previous project)
Show optimal path generation animation between start and goal point using a simple graphical interface. You need to show both the node exploration as well as the optimal path generated.
The visualization of (exploration and optimal path) should start only after the exploration is complete and optimal path is found.
Note: A separate document will be provided later this coming week to describe this step

## Slide 15: Step 5 (continue): Display the graph in the configuration space
Use a line to connect the new node to previous nodes and display it on the Map as the search space is explored.
The visualization of the optimal path will start once your algorithm has found the optimal path using A*.
Exploration and Optimal Path should be in different colors.
Sample code for visualization is provided.

## Slide 16: Visualization

## Slide 17: Step 6) Display the optimal path in the map

## Slide 18: Final Map
Origin
x
y

## Slide 19: Deliverables
Deliverables:
ReadMe.txt (Describing how to run the code in a txt format)
Source files
  Student_name.py
  GitHub repository link in the URL submission (private repository)
Output
  Video recording (start and goal point can be random)
  Note: The code should accept start and goal points from the user